## Slide 1: Adoption Rates for Irrigation Practices in the Mid-south
C.G. Henry, L.J. Krutz, J. Henggeler, R. Levy
RISER

## Slide 2
Survey represents 1.02 Million irrigated acres, there are 13.3 Million acres reported in the region by NASS (8% sample)
Margin of error, 4.6%, 95% CI, 50% Response Distribution

## Slide 3
Chart: State Response to USB Irrigation survey
| Mississippi | Arkansas | Lousianna | Missouri
 | 31.8 | 42.7 | 20 | 5.6

## Slide 4: Survey Questions
2016 crop year
Perceptions about water shortage
IWM practices: CHS, Surge, Irrigation Scheduling methods
Pumps, energy sources, etc.
Crop types, irrigation systems, etc.
Demographics

## Slide 5
Chart: Do you have a groundwater shortage problem in your state?
| Yes | No | Don't know | Refused
 | 44.6 | 36.1 | 18.7 | 0.6
 | 0

## Slide 6: On a scale of 1 to 5, with 1 meaning 'no problem' and 5 meaning 'severe problem,' how would you rate the groundwater shortage problem on your farm?
3.49

## Slide 7
Chart: Do you have a groundwater shortage problem on your farm?
| Yes | No | Don't know | Refused
 | 9.7 | 89.3 | 0.9 | 0.2
 | 0

## Slide 8
Chart: Do You Use CHS on your Farm?
| Yes | No | Don't Know | Refused
 | 40.7 | 58.4 | 0.7 | 0.2

## Slide 9
83.2% since 2012 when DeClerk, Henry, Krutz, Reba started
Chart: What Year Did You Start Using CHS?
| 2016 | 2015 | 2014 | 2013 | 2012 | 2011 | 2010 | 2009 | 2008 | 2006 -1983
 | 12.8 | 22.9 | 17.9 | 16.8 | 12.8 | 4.5 | 2.8 | 1.1 | 2.8 | 5.8

## Slide 10
Chart: What is the primary reason you started using CHS?
| Learned about ... Extension meeting | I wanted to reduce input costs | I tried it on my farm and saw the benefit | Other | Learned about ... industry meeting | Experienced water shortage on farm, needed to increase capacity | Heard about this technology from a neighbor | Profit allowed for new investment in technology
 | 24.6 | 20.1 | 19.6 | 19 | 5.6 | 3.9 | 3.9 | 3.4

## Slide 11
Chart: What is the Primary Reason you are not using CHS?
| Other | It doesn't work on my farm | Was not aware of the technology | Don't know how to use it | Fuel, labor and equipment cost too high | Would like to, not sure how | Takes too much time to implement | Groundwater is adequate | Surface Water is adequate | Crop Prices too low | Don’t know | Refused
 | 26.1 | 15.6 | 14 | 11.3 | 9.3 | 7.8 | 6.6 | 4.7 | 1.6 | 1.6 | 0.8 | 0.8

## Slide 12
Chart: Other Reasons farmers do not use CHS
| Doesn't need it | Not interesed | Too old to change to new technology | Pivot is best for their type of farm | Planning to use it next year | Farm too small | We do not use computer technology
 | 17 | 12 | 8 | 6 | 6 | 2 | 2

## Slide 13: Other reasons why they don’t use CHS
The computer doesn't know if a phaucet uses more water than the others
Its a new system to the area
Knows the size of the holes he needs on his farms (3)
Knows the soil well enough to predict what size the holes needed
Wells surge and cannot get accurate reading to determine holes size
It's not accurate
It was not how it was set up when he got it

## Slide 14
Chart: Have you ever used Surge Irrigation?
| Yes | No | Don't know
 | 21.1 | 77.7 | 1.1

## Slide 15
Chart: What are the reasons you are not using surge irrigation?
| It doesn't work on my farm | Was not aware of the technology | Other | Fuel, labor and equipment cost too high | Don't know how to use it | Would like to, not sure how | Groundwater is adequate | Surface Water is adequate | Don’t know | Takes too much time to implement | Crop Prices too low
 | 25.4 | 20.8 | 13.2 | 11.4 | 9.9 | 7.3 | 5.6 | 2 | 1.8 | 1.5 | 1.2

## Slide 16: Other Methods
30% report using end blocking
10.5% report using cutback irrigation
54.8% report using deep tillage

## Slide 17: Center Pivots
16% of acres under pivot
8.7 years between sprinkler package changes
62.3 percent of Center Pivots in Arkansas have drop nozzles
79.5% have end guns
Only 33.5% of pivots have rotators
6.5% have VRI
4.2% have corner units
14.2% are considering converting their CP to furrow, representing 3% of irrigated acres in the mid-south

## Slide 18
Chart: Do you have a timer on your pumps?
| Yes | No
 | 27.7 | 72.1
15% of pumps have timers

## Slide 19
Chart: Do you own any Flow Meters?
| Yes | No | Prefer not to answer
 | 42.2 | 57.4 | 0.4

## Slide 20
Chart: Which of the following methods do you use to schedule irrigation on your farm?
| Visual crop stress | Routine | Soil Moisture Sensors | Probe or feel method | Watch Neighbor | computerized scheuler | ET or Atmometer | Woodruff charts | Canopy temp
USB | 72 | 27.7 | 23.4 | 21.8 | 5.5 | 4.1 | 2.5 | 0.9 | 0.5
NASS | 93.3048 | 15.6686 | 6.035 | 50.1116 | 5
USB (2016); NASS (2012)

## Slide 21
Chart: When did you start using soil moisture sensors?
| 2016 | 2015 | 2014 | 2013 | 2012 | 2011 | 2008
 | 21.4 | 18.4 | 25.2 | 21.4 | 6.8 | 4.9 | 1

## Slide 22
This represents an adoption rate of 17%
for all irrigated acres (rice acres excluded)
But Houston, we have a problem,
55% don’t know what brand they are using

## Slide 23
Chart: Rice Production Systems
| Precision Grade | Contour Levee | Zero Grade | Furrow Rice | Sprinkler Rice
 | 0.54452 | 0.25533 | 0.084749 | 0.096526 | 0.018875

## Slide 24
Chart: Adoption of MIRI
| Precision Grade MIRI | Contour Levee MIRI
 | 0.47519 | 0.70944

## Slide 25
Chart: When did you start using MIRI
| 1949-1986 | 1990-2001 | 2002-2006 | 2007-2011 | Since 2012
 | 20.6 | 15.1 | 20.2 | 23.7 | 18.7

## Slide 26
Chart: What is reason you started MIRI?
| I tried it on my farm and saw the benefit | I wanted to reduce input costs | Learned about technology from Extension Meeting | Experience water shortage on farm, needed increased capacity | Other | Water Efficiency | Heard about technology from a neighbor | Profit allowed for new investment in technology | Conservation district offered new technology | Don’t know | Learned about technology from Industry | More rapid flood
 | 0.35252 | 0.19424 | 0.086331 | 0.079137 | 0.071942 | 0.05036 | 0.043165 | 0.028777 | 0.028777 | 0.028777 | 0.021583 | 0.014388

## Slide 27
Chart: What is reason you are not using MIRI?
| Rental agreement does not allow | Damage to pipe during season too much to keep repaired | Was not aware of MIRI | Don't know how to use it | Surface Water is adequate | Do not have a reason to use it | Fuel, labor, and equipment cost is too high | Don't know | Takes too much time | Would like to use, but not sure how to get started | Groundwater is adequate | Other | It doesn’t work on my farm
 | 0.015625 | 0.015625 | 0.03125 | 0.03125 | 0.03125 | 0.03125 | 0.046875 | 0.046875 | 0.0625 | 0.078125 | 0.14062 | 0.14062 | 0.32812

## Slide 28
Chart: Soil Management to improve Irrigation
| Gypsum | PAM | Deep Tillage | Cover Crops
 | 0.010801 | 0.0041451 | 0.30369 | 0.3

## Slide 29
Chart: Water Savings from Irrigation Practices
| CHS | Center Pivots | Deep Tillage | End Blocking | Surge | Irrigation Scheduling | MIRI | Reservoirs | Zero Grade
 | 0 | 4.3709 | 6.2216 | 9.4667 | 10.5135 | 12.6526 | 13.3315 | 13.8 | 22.6275

## Slide 30: Take Home Message
Hey guys, the state has a serious water problem, but it’s not on my farm.
Major improvement in CHS practices showed up in survey, likely due to DP and Extension programs for Pipe Planner.
“Doesn’t work on my farm” or “Doesn’t need it” most reported excuse to CHS
“Doesn’t work on my farm” or “Don’t know how to use it” most reported excuse for not using MIRI
MIRI adoption is high, but questionable.
If they tried it and saw the benefit, they adopted it.
They also appear to adopt practices because of Extension meetings.
Perception is that water savings are small; reason for doing them is to reduce production costs